## Slide 1
The Design, manufacturing, and implementation of a Ka-band pyramidal horn antenna, using advanced additive manufacturing techniques
Student name: Alec Robin Gould
Student number: 16412117
Supervisor: Professor Mbuyu
Module name: Research Project 1B (HMELE80)
Department: Department of Electrical and Smart Systems Engineering
Date:03/10/2025

## Slide 2: Background
Traditional horn antennas: milling, casting, turning
  Limitations: complex geometries, cost, time
  Additive manufacturing enables intricate, optimized designs
  Potential for material savings and cost reduction

## Slide 3: Problem statement
Conventional manufacturing struggles at Ka-band (26.5–40 GHz)
  High precision needed as frequency increases
  Need for cost-effective, flexible, high-performance alternatives

## Slide 4: Aim and Objectives
Design, manufacture, and optimize Ka-band pyramidal horn antenna
  Use SLA 3D printing + palladium-free electroless plating
  Validate through HFSS simulations and measurements

## Slide 5: Literature Review
AM in antennas: enables new geometries
  Ka-band use cases: satellite, radar, remote sensing
  Previous plating: Pd-based, costly – need Pd-free approach

## Slide 6: Theoretical Background
Horn antennas: waveguide-to-free-space impedance transition
  Pyramidal horns: stable patterns, broadband gain
  Field equations define E/H fields, aperture integration

## Slide 7: Modeling and Validation
Three design approaches: Traditional, Optimum, Tuned
  Formulas define flare dimensions
  Validated via HFSS simulations

## Slide 8: Simulation
Simulated horns with Ansys HFSS
  Performance nearly identical across variants
  Key metrics: reflection coefficient (S11), gain (S21)

## Slide 9: Presentation & Analysis of results
Six antennas 3D printed + copper plated
  Reflection coefficients measured (Agilent 8510C VNA)
  Performance comparable to simulations (within 2–8 dB)

## Slide 10: Analysis
3D printed horns feasible for Ka-band
  Measured vs simulated: small deviations due to flange/coupling
  Tuned variant performed best (-24 dB S11)

## Slide 11: Discussion
3D printing: offers flexibility but tolerances critical
  Plating: Pd-free process worked, adhesion verified
  Future: include radiation pattern measurement

## Slide 12: Challenges Encountered
Balancing support material vs. minimal post-processing
  Surface prep and plating chemistry required fine control
  Variation between samples: process consistency needs work

## Slide 13: Budget
3D printing resin and consumables: low cost
  Chemicals for plating: inexpensive, Pd-free
  Equipment (HFSS, VNA, adapters) already available

## Slide 14: Conclusion
SLA 3D printing + Pd-free plating successful at Ka-band
  Performance close to traditional horns
  Promising for cost-effective mm-wave antenna research